Acknowledgments

This cruise and preliminary data report was prepared by Richard Limeburner. We thank the officers and crew of the R/V Oceanus Cruise 345 for their skill and superb assistance that made possible the recovery of 8 moorings and completion of the hydrographic survey. Special thanks to Wil Ostrom for leading the successful mooring deployment operation and George Tupper for maintaining and operating the shipboard scientific equipment and coordinating this instrumentation with the needs of the scientific party.

The GLOBEC research effort is sponsored by the National Science Foundation and the National Oceanic and Atmospheric Administration. Support for Frontal Exchange Processes over Eastern Georges Bank Program as part of the U.S. GLOBEC Northwest Atlantic/Georges Bank Study was provided by NSF research grant OCE-98-06379. All data and results in this report are to be considered preliminary.

Cruise Report

GLOBEC R/V OCEANUS OC345

# Table of Contents

## Table of Contents									2

Purpose and Accomplishment Summary						3

Cruise Results										4

1. Frontal Study Moorings								4

1.1 North Flank Shallow – Mooring site NFS				4

1.2 Eastern Flank – Mooring site EF						4

1.3 North Flank Deep – Mooring site NFD					4

2. Hydrography							            5

2.1 Calibration								            5

2.2 Hydrographic Station Locations					            6

2.3 Near-surface Temperature and Salinity Profiles			            6		2.4 T/S plot of all stations						            8

Cruise Event Log								            9

Cruise Personnel								          11

Chief Scientist’s Log of Daily Events					          11

Appendix 1 – CTD station profile data 					          14

Lists of Figures

Figure 1. R/V Oceanus OC345 Cruise Track and Mooring Locations.

Figure 2. CTD Conductivity Sensor calibration

Figure 3. Oceanus 345 CTD station locations

Figure 4. Surface temperature and Salinity, August 1-6, 1999

Figure 5. T/S plot of all CTD stations.

Figures 6-22. CTD profile data

# Preliminary Cruise Report

### GLOBEC R/V OCEANUS – OC345

US State Department Cruise No. 99-013

Woods Hole to Georges Bank to Woods Hole

August 1-6, 1999

#### Purpose

The primary purpose of OC345 was to recover instrumented moorings at several sites on the northern and eastern flank of Georges Bank and to conduct CTD and ADCP surveys over the eastern half of the Bank. This NSF program, Frontal Exchange Processes Over Eastern Georges Bank, was designed to focus on frontal processes, which occur over eastern Georges Bank in winter through spring. In particular we want to examine (a) the flow of water and biota onto the Bank along the northeastern flank driven by the strong local semidiurnal tidal currents (which can reach 1.5 m/s during spring tide), winter storms, and the seasonally-evolving density field, and (b) the advection of Scotian shelf water across the Northeast Channel onto the Bank associated with the shelf/slope front and episodic events such as winds and buoyancy pulses.

#### Accomplishment Summary

The cruise successfully recovered 8 moorings at 3 sites over the north and east flanks of  Georges Bank. The ship’s track, mooring locations, and CTD station locations are shown in Figure 1. A total of 33 CTD stations were made during the cruise.

Figure 1. OC345 cruise track, CTD station and mooring locations.

#### Cruise Results:

- Frontal Study Moorings – Dick Limeburner and Charlie Flagg

1.1 North Flank Shallow - Mooring Site NFS

#### The ship arrived at the NFS mooring site at 1800Z on 8/2/99 and we immediately made a CTD cast. Preparation for recovery of NFS guard buoy  C began after the CTD cast and the recovery was completed at 1910Z. There was a large knot of chain near the anchor and about 78 m of chain were measured between this chain knot and the mooring swivel. NFS guard buoy A was recovered  at 2058 Z and again there was a large chain knot near the anchor located about 72 m below the wire rope. The NFS subsurface mooring was recovered at 2218Z and all the subsurface instrumentation appeared in good condition. A GPS drifter with drogue centered at 10 m was deployed near the NFS site at 2255Z and we then began making CTD stations along a north/south line passing through the NFS and NFD sites.

#### At 1020 Z on August 31, 1999 we began recovering the NFS discus mooring. Large tensions were apparent during the recovery and we believe the NFS discus ground chain was also wrapped in a knot near the 5000 lb anchors. We disconnected the mooring below the lowest instrument and steamed to the EF mooring site

  - Eastern Flank - Mooring Site EF

The guard buoy at the EF mooring site was recovered on August 2, 1999 at 1429Z along with a small fisherman’s buoy. We then began recovering the EF discus mooring at 1658Z. A piece of polypropylene fishnet was caught in the discus bridle and needed to be cut away in order to disconnect the EF discus from the rest of the mooring. We disconnected the mooring below the lowest instrument and began an east/west CTD section during the evening.

1.3 North Flank Deep – Mooring Site NFD

At sunrise on August 3, 1999 we released the anchor on the ADCP frame, but the instrument package remained on the bottom at the NFD site. We decided to recover the NFD discus and then begin dragging operations for the bottom mounted ADCP. The NFD discus was on the deck at 1233Z. Fish line was attached to the discus bridle as well as a collapsed polyform buoy. We disconnected the mooring below the lowest instrument and began the dragging operation for the ADCP. At 1824Z the ADCP surfaced after one hour of dragging and at 1851Z the ADCP was on the deck. Table 1 summarizes the mooring recoveries.

| Mooring | ID | Date | Time UTC | Latitude N | Longitude W | Depth m |
| --- | --- | --- | --- | --- | --- | --- |
| North Flank Shallow Guard | NFSC | 8/2/99 | 1930 | 42( 04.80’ | 66( 42.00’ | 74 |
| North Flank Shallow Guard | NFSO | 8/2/99 | 2104 | 42( 04.71’ | 66( 42.27’ | 74 |
| North Flank Shallow SubSurf. | NFSSS | 8/2/99 | 2223 | 42( 04.60’ | 66( 41.93’ | 72 |
| North Flank Shallow Discus | NFS | 8/3/99 | 1022 | 42( 04.49’ | 66( 42.04’ | 76 |
| East Flank Guard | EF | 8/3/99 | 1432 | 41( 44.29’ | 66( 06.78’ | 97 |
| East Flank Discus | EF | 8/3/99 | 1658 | 41( 44.31’ | 66( 06.53’ | 100 |
| North Flank Deep Discus | NFD | 8/4/99 | 1233 | 42( 09.79’ | 66( 42.19’ | 160 |
| North Flank Deep ADCP | NFD | 8/4/99 | 1851 | 42( 10. 25’ | 66( 42.57’ | 160 |

#### Table 1. OC345 mooring recovery times and positions.

2.   HYDROGRAPHY – Dick Limeburner

#### 2.1 Calibration

Standard CTD data was collected during Oceanus 345 with a Sea Bird Electronics SBE-911 profiling CTD measuring pressure, conductivity, temperature, light transmission, fluorescence, turbidity and irradiance. At least one seawater sample was collected at each station for calibration of the conductivity sensor on the SBE-911 CTD. Figure 2 below summarizes the comparison between the conductivity measured by the CTD and the in situ conductivity calculated from the water sample bottle salinity using a Guildline Salinometer. The RMS conductivity difference was 0.0032 s/cm and this offset was not applied to the data.

Figure 2. Differences between the CTD conductivity and the seawater sample conductivity during the cruise.

2.2 Hydrographic Station Locations

A total of 33 CTD stations were completed during the cruise along 3 sections radiating outward from the center of the eastern flank of Georges Bank. The locations of the CTD stations are shown in Figure 3.

Figure 3. CTD station locations during OC345.

2.3 Surface Temperature and Salinity and Profiles

Near-surface temperature and salinity over the eastern flank of Georges Bank during OC333 are shown in Figure 7.

Figure 4. Surface temperature and salinity.

#### 2.4	T/S Plot of all stations.

#### Figure 5. T/S plot of all the stations on OC345.

#### Oceanus 345 Cruise Event Log

| Event | Instrument | Cast # | Station | Year | Month | Day | Hr:mn | S/E | N. Lat | W. Lon | Cast | Water | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | UTC |  |  |  | Depth m | Depth m |  |
| 1 | SBE-911 | 1 | NFS | 1999 | 8 | 2 | 1814 | S | 420 04.57' | 660 42.60' | 69 | 74 | Bottle V1 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 2 | NFS Guard |  | NFSC | 1999 | 8 | 2 | 1910 | S | 420 04.80' | 660 42.00' |  | 74 | Recover mooring |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 3 | NFS Guard |  | NFSO | 1999 | 8 | 2 | 2104 | S | 420 04.71' | 660 42.27' |  | 74 | Recover mooring |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 4 | NFS SS |  | NFSSS | 1999 | 8 | 2 | 2223 | S | 420 04.60' | 660 41.93' |  | 72 | Recover mooring |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 5 | SBE-911 | 2 | NF1 | 1999 | 8 | 3 | 0119 | S | 420 19.2004' | 660 42.0026' | 295 | 299 | Bottle V2 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 6 | SBE-911 | 3 | NF2 | 1999 | 8 | 3 | 0210 | S | 420 14.2647' | 660 41.9509' | 241 | 245 | Bottle V3 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 7 | SBE-911 | 4 | NF3 | 1999 | 8 | 3 | 0246 | S | 420 12.2532' | 660 42.0248' | 211 | 216 | Bottl3 V4 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 8 | SBE-911 | 5 | NF4 | 1999 | 8 | 3 | 0314 | S | 420 11.0061' | 660 41.9803' | 197 | 203 | Bottle V5 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 9 | SBE-911 | 6 | NF5 | 1999 | 8 | 3 | 0342 | S | 420 09.5222' | 660 42.0207' | 123 | 133 | Bottle V6 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 10 | SBE-911 | 7 | NF6 | 1999 | 8 | 3 | 0406 | S | 420 08.3969' | 660 42.0367’ | 96 | 99 | Bottle V7 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 11 | SBE-911 | 8 | NF7 | 1999 | 8 | 3 | 0431 | E | 420 07.0475' | 660 42.0226' | 69 | 75 | Bottle V8 |
| 12 | SBE-911 | 9 | NF8 | 1999 | 8 | 3 | 0503 | S | 420 04.8200' | 660 42.0378' | 66 | 72 | Bottle V9 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 13 | SBE-911 | 10 | NF9 | 1999 | 8 | 3 | 0555 | E | 410 59.5403' | 660 39.5159' | 70 | 75 | Bottle V10 |
| 14 | SBE-911 | 11 | NF10 | 1999 | 8 | 3 | 0642 | E | 410 54.7969' | 660 37.0508' | 71 | 75 | Bottle V11 |
| 15 | SBE-911 | 12 | NF12 | 1999 | 8 | 3 | 0727 | S | 410 49.7380' | 660 34.7605' | 72 | 77 | Bottle V12 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 16 | NFS Discus |  | NFS | 1999 | 8 | 3 | 1021 | S | 420 04.49' | 660 42.04' |  | 76 | Recovered |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 17 | SBE-911 | 13 | EF | 1999 | 8 | 3 | 1406 | S | 410 44.1840' | 660 06.7385' | 88 | 93 | Bottle V13 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 18 | EF Guard |  | EF | 1999 | 8 | 3 | 1433 | S | 410 44.1840' | 660 06.7385' | 88 | 93 | Recovered |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 19 | EF Discus |  | EF | 1999 | 8 | 3 | 1658 | S | 410 44.31' | 660 06.53' | 88 | 93 | Recovered |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 20 | SBE-911 | 14 | EF | 1999 | 8 | 3 | 2031 | S | 410 48.1349' | 650 38.4337' | 995 | 1050 | Bottle V14 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 21 | SBE-911 | 15 | EF | 1999 | 8 | 3 | 2205 | S | 410 47.2637' | 650 45.2522 | 155 | 160 | Bottle V15 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 22 | SBE-911 | 16 | EF | 1999 | 8 | 3 | 2239 | S | 420 46.7000' | 650 52.8328' | 121 | 125 | Bottle V16 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 23 | SBE-911 | 17 | EF | 1999 | 8 | 4 | 0020 | S | 410 46.1242' | 650 58.9482 | 100 | 103 | Bottle V17 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 24 | SBE-911 | 18 | EF | 1999 | 8 | 4 | 0109 | S | 410 45.6255' | 660 05.7546' | 90 | 93 | Bottle V18 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 25 | SBE-911 | 19 | EF | 1999 | 8 | 4 | 0153 | S | 410 45.1591' | 660 12.2679' | 85 | 89 | Bottle V19 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 26 | SBE-911 | 20 | EF | 1999 | 8 | 4 | 0236 | E | 410 44.750' | 660 18.1362' | 78 | 84 | Bottle V20 |
| 27 | SBE-911 | 21 | EF | 1999 | 8 | 4 | 0314 | S | 410 43.2305' | 660 41.6853' | 73 | 76 | NFS site,Bot AJ18@73m |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 28 | SBE-911 | 22 | NEP | 1999 | 8 | 4 | 0354 | E | 410 43.6548’ | 660 32.3612' | 68 | 73 | Bottle V22 |
| 29 | NFD Discus |  | NFD | 1999 | 8 | 4 | 1233 | S | 420 09.79’ | 660 42.19’ | 160 |  | Recovered |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 30 | NFD ADCP |  | NFD | 1999 | 8 | 4 | 1851 | S | 420 10.25’ | 660 42.57' | 160 |  | Recovered |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 31 | SBE-911 | 23 | NEC | 1999 | 8 | 4 | 2235 | S | 420 18.0691’ | 650 50.1784 | 210 | 215 | Bottle V23 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 32 | SBE-911 | 24 | NE | 1999 | 8 | 4 | 2324 | S | 420 14.1636’ | 650 53.1036’ | 235 | 240 | Bottle V24 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 33 | SBE-911 | 25 | NE | 1999 | 8 | 5 | 0019 | S | 420 10.2168' | 650 58.3961 | 222 | 224 | Bottle V25 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 34 | SBE-911 | 26 | NE | 1999 | 8 | 5 | 0101 | S | 420 08.0081’ | 660 01.3598’ | 212 | 220 | Bottle V26 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 35 | SBE-911 | 27 | NE | 1999 | 8 | 5 | 0138 | E | 420 05.4109' | 660 04.5258’ | 123 | 128 | Bottle V27 |
| 36 | SBE-911 | 28 | NE | 1999 | 8 | 5 | 0215 | E | 420 01.9473’ | 660 08.9290’ | 89 | 93 | Bottle V28 |
| 37 | SBE-911 | 29 | NE | 1999 | 8 | 5 | 0249 | E | 410 58.2042’ | 660 13.1959’ | 79 | 83 | Bottle E1 |
| 38 | SBE-911 | 30 | NE | 1999 | 8 | 5 | 0325 | E | 410 54.6725’ | 660 18.0566’ | 77 | 83 | Bottle E2 |
| 39 | SBE-911 | 31 | NE | 1999 | 8 | 5 | 0356 | S | 410 51.1255’ | 660 22.4207' | 75 | 80 | Bottle E3 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 40 | SBE-911 | 32 | NE | 1999 | 8 | 5 | 0433 | S | 410 37.3297 | 660 26.7083’ | 73 | 78 | Bottle E4 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |
| 41 | SBE-911 | 33 | NE | 1999 | 8 | 5 | 0513 | S | 410 44.2765’ | 660 31.8416’ | 69 | 73 | Bottle E5 |
|  |  |  |  |  |  |  |  | E |  |  |  |  |  |

#### Cruise Personnel

#### Scientific Crew

Richard Limeburner, Chief Scientist

Charles Flagg, Scientist

Wil Ostrom, Senior Engineer

Larry Costello, Engineer

Jim Dunn, Engineer

Claudia Cenedese, Post doc

Natasha Grey, NSF Biology

Rochelle Ugstad, Electonic Engineer

Erica Rude, Electronic Engineer

Kristin France, Student

Rachael Stanley, Student

Andrew Thompson, Student

Alex Walsh, EPaint representative

#### Ship’s Crew

Lawrence Bearse, Captain

Richard Chase, Chief Mate

## Emily Sheasley, 2nd Mate

Horace Madeiros, Boatswain

James Ryder, AB

Peter Liarikos, OS

Patrick Pike, AB

Richard Morris, Chief Engineer

Alberto Collasius, Jr. Engineer

John Kay, Jr. Engineer

Torii Corbett, Steward

##### Benjamin Malarkey, Mess Attendant

### Chief Scientist’s Daily Log

#### Sunday – August 1, 1999

EST

1600 – Depart WHOI dock

1630 – Fire and boast drill

1700 – Science meeting

Monday – August 2, 1999

EST

0830 – Wil gave class on deck work

1400 – Arrive at mooring location NSF

1415 – CTD 1 at NFS

1510 – Recovered NFS Guard C

1658 – Recovered NFS Guard O

1818 – Recovered NFS Subsurface

1855 – Deployed GPS drifter 24947

2119 – CTD 2 – Begin north section CTD line

2210 – CTD 3

2246 – CTD 4

2314 – CTD 5

2342 – CTD 6

Tuesday – August 3, 1999

EST

0006 – CTD 7

0031 – CTD 8

0103 – CTD 9

0155 – CTD 10

0242 – CTD 11

0327 – CTD 12

0620 – Recovered NFS Discus

1006 – CTD 13

1029 – Recovered EF Guard

1258 – Recovered EF Discus

1631 - CTD 14

1805 – CTD 15

1839 – CTD 16

2020 – CTD 17

2109 – CTD 18

2153 – CTD 19

2236 – CTD 20

2314 – CTD 21

2354 – CTD 22

Wednesday – August 4, 1999

EST

0833 – Recovered NFD Discus

1105 – 1424 - Dragged for ADCP

1451 – Recovered ADCP

1835 – CTD 23

1924 – CTD 24

2019 – CTD 25

2101 – CTD 26

2138 – CTD 27

2215 – CTD 28

2249 – CTD 29

2325 – CTD 30

2356 – CTD 31

Thursday – August 5, 1999

EST

0033 – CTD 32

0113 – CTD 33

Friday – August 5, 1999

EST

0000 – 0400 – Steamed along cross-shelf line for Paula Fratantoni

0845 – Tied up at WHOI dock

Appendix 1. CTD Station Profile Data