REPORT ON C.S.S. Parizeau CRUISE 97-025

27 June-4 July, 1997

by

Peter C. Smith and Gary L. Bugden

Ocean Sciences Division

Bedford Institute of Oceanography Dartmouth, Nova Scotia

CANADA

July, 1997

BEDFORD INSTITUTE OF OCEANOGRAPHY CRUISE REPORT Parizeau 97-025

Local Cruise Designation:	97-025

Vessel:	C.S.S. Parizeau

Dates:	27 June-4 July, 1997

Area:	Southwest Nova Scotia/Georges Bank

Responsible Agency:	Ocean Sciences Division

Scotia-Fundy Region, DFO

Ship's Master:	Capt. G. O’Donnell

Scientific Personnel:

P.C.Smith	Ocean Sciences

M. Scotney	Ocean Sciences

G. Bugden	Ocean Sciences

L. Bellefontaine	Ocean Sciences

B. Nickerson	Ocean Sciences

M. Coombs	Harding Scientific

M. Buehner	Dalhousie U.

1. PURPOSE

The scientific objectives of this cruise were:

1)	long term monitoring of the major inflows to the Gulf of Maine, namely the surface inflow from the Scotian Shelf off Cape Sable and the deep inflow of slope water through Northeast Channel,

2)	determining the seasonal hydrographic properties along the eastern boundary of the Gulf of Maine, and

3)	measuring the hydrographic structure over Truxton Swell and in Jordan Basin (if possible) in order to determine the extent of slope water penetration into Jordan Basin.

The activities planned for the cruise period include:

1)	recovery of moorings in Northeast Channel (NECE,NECW), on southeastern Georges Bank (SEF), and on northeast peak (WHOI mooring plus guard buoy),

2)	CTD survey along the eastern boundary of the Gulf of Maine,

including Browns Bank, Northeast Channel, Georges Basin and Truxton Swell and along the Halifax Section, and

3)	repeated ADCP transects across Northeast Channel over at least one tidal cycle.

2. NATURE OF DATA GATHERED

During this cruise, a total of four complete BIO current meter moorings and two guard buoys were recovered at three sites in the Gulf of Maine (NECE, NECW, SEF; see Figure 1a and Table 1).  The bottom portion of one mooring (#1242) at NECE and the top portion of another (#1241) at NECW were also recovered; the floats on #1242 had been recovered earlier in Portsmouth, NH, and the bottom instrument, release and tide gauge on #1241 were lost.  Only one guard buoy was found at both NECE and NECW; and all three were missing from SEF.  In addition to the BIO moorings, a WHOI instrument mooring (“B”) and guard buoy (“A”) were successfully recovered from the northeast peak site (NEP, see Figure 1a).  An engineering mooring was also recovered from Emerald Basin (43o 53.17’N, 62o 51.89’W) on the way into BIO.

In addition, a total of 51 CTD stations (Fig.1b, Table 2) were occupied along:

1)	a section from the 50 m isobath off Cape Sable to the outer edge of Browns Bank (Fig.3),

2)	a section across Northeast Channel from Browns to Georges Bank (Fig.4),

3)	a section across the western flank of Browns Bank (Fig.5),

4)	a section along Truxton Swell (Fig.6)

5)	a section following the 200 m isobath on the eastern side of the Channel, from Truxton Swell to the mouth (Fig.7),

7)	a section across the outer Scotian Shelf off Shelburne (Fig.8),

8)	the Halifax Section (Fig.9), and

9)	at each mooring site.

The quality of the CTD temperature and salinity measurements is quite acceptable (Table 2a), especially considering the relatively high variability of the standards used. The YSI dissolved oxygen sensor showed a large offset with respect to the titrated values from near-bottom samples (Table 2a; Fig.2a), but stable calibrations were obtained by linear regression of sensor vs. titrated values (Table 2b).  The YSI sensor exhibited occasional noise, spikes, and hysteresis between the up- and downtraces.  In addition, roughly 200 oxygen isotope samples were collected throughout the water column at even numbered stations (Fig.1b) for Dr. Robert Houghton of Lamont-Doherty Earth Observatory.  Nutrient samples were collected throughout the water column as well at the even-numbered stations.

Ten repeated ADCP transects (6 full, 4 partial; Table 3) were run over the duration of the cruise along the mooring/CTD line in Northeast Channel (Fig.1b) in order to monitor the inflow/outflow over an M2 tidal cycle.  A total of (16 hrs was devoted to straight-run transects, with an additional 20 hrs spent on the CTD and mooring lines.  Only processed (averaged) data were collected over the entire cruise  and stored as 5-min averaged data files.  At the start of the cruise, a test of the ADCP transducer alignment error and amplification factor showed that these values were acceptable (Table 3a.) .

3. PROGRAM SUMMARY

Date	From(UTC)	To(UTC)	Operation

27 June	1300	2100	Windlass breakdown delays departure

2100	1500(28)	Depart BIO enroute to NECE mooring site

28 June	1500	0100(29)	Mooring recovery operations at NECE, NECW;

CTD1,2

29 June	0153	0513	CTD3-6 on Section Ib

0900	1430	Mooring recovery operations at NEP,SEF;

CTD7-8

1700	1850(1)	CTD9-37 on Sections Ia,Ib,II,III and V

1 July	1850	1020(2)	Repeated ADCP transects across NEC

2 July	0900	0100(3)	CTD38-44 on Sects.V, VI

3 July	1230	0300(4)	CTD45-51 on Halifax Sect.; recover test mooring

4 July		1000	Arrive BIO

4. MOORING OPERATIONS

The recovery of four of the six BIO instrument moorings at three sites (SEF, NECW and NECE; Table 1, Appendix) was completed without incident.  Using differential GPS positioning with AGCNAV and transponding with the release, it was possible to locate and retrieve all of the moorings quickly.  One partial mooring (#1242 at NECEA), consisting of the two instruments backup buoyancy (BUB) and the release, was also recovered routinely.  The Fairey floats had been reported found in Portsmouth, NH on June 11. The termination of the upper segment of wire rope had parted and the wire ends appeared to be corroded badly.  In addition, some fishing line was hooked into the release, suggesting some further stress on the components.  The deep mooring at site NECW (#1241) was contacted and released, but did not come to the surface.  A subsequent survey revealed that the release was upright and NW of its original position by 0.1nm. A subsequent dragging operation (~1200m drag wire encircling the mooring twice at radii of 0.2 and 0.1 nm) was partially successful.  As the drag was hauled in, it encountered a large strain, then released.  The Fairey float and two streamline packages then came to the surface, along with a single glass ball indicating the BUB had been damaged.  On recovery, it was discovered that the mooring had parted just below the deeper streamline package, leaving the deep instrument, BUB, release and tide gauge behind.  Interrogation of the release indicated that it was no longer upright, suggesting it had parted from the BUB as well.  Record dumps of the instruments indicate that the mooring had been hit only recently (mid-Sept.).  Otherwise, all the returning moorings were in relatively good shape.  There were major(minor) amounts of hairy growth on the instruments at the 20m(50m) levels, but the conductivity cells and rotors were clean.  The “killing tubes” on the SEACATs seemed to work well, and painting the entire RCM case with antifoulant kept the growth away from the rotor and conductivity cell, except in the case of instrument RCM2664 on the SEF mooring.  Here the hairy growth on the handle of the instrument was sufficient to impede the rotor when the instrument came aboard. Each had the expected number of words in memory.

Of the original eleven guard buoys, one was found at each of the NECW and NECE sites, and none of the three at SEF or two at NEP was found.  One possible explanation for this is the quality of the splices in the nylon braid rope components of the mooring lines.  The line on the NECE guard buoy parted at the upper splice as it was being hauled in (leaving the thimble behind) and the upper splice on the NECW guard buoy looked very frayed and weakened.  This would be consistent with the complete loss of the shallower guards, since the stronger tidal currents on the bank would work the splice harder.

Problems/Recommendations:

(1)	Investigate means to improve the splicing of the nylon braid in the guard buoy mooring lines in future.

5. HYDROGRAPHIC MEASUREMENTS

Hydrographic and chemical measurements were made at a total of 51 stations (Table 2) using a Seabird 9/11 Plus system, equipped with a SBE 23Y Yellow Springs Instruments (YSI) dissolved oxygen sensor.  The data were logged on a 33 Mhz 486 PC and post-processed between stations using SEABIRD's software.  Once processed, the data were transferred to the VAX over the network for final tape backup to EXABYTE.

Water column sampling was accomplished with a General Oceanics 12-bottle rosette (only 9 slots were available because of instrument). Duplicate nutrient and oxygen isotope samples were drawn at roughly standard depths on the even numbered stations only.  In addition, two calibration bottles were tripped at the bottom of each cast for temperature, salinity and dissolved oxygen (see below).

Several electrical problems were encountered with the CTD system during the course of the cruise.  Early in the cruise, the error lights shone frequently during the stations, although the data appeared to be good.  Various fixes included a new deck unit, new splice, and a new probe.  Later, the bottle trip indicators failed, although the bottles did fire on command, but no calibration information was captured by the system.  To get around this problem, a manual procedure involving SEABIRD’s MARKSCAN routine was instituted with appropriate modifications to the process deck.  The main problem appears to be the aging GO rosettes, which are failing both electronically and mechanically.

5a. Processing

The processing and data transfer to the VAX was initiated by a single command at the end of the station.  This command, called PROCESS, starts a batch job that sequentially passes the data through a number of programs. Most were from SEABIRD's SEASOFT package.  A few were custom written at BIO.  The following is a summary of the processing procedure [modifications required for the manual bottle trip procedure are indicated in square brackets]:

(0)	[Run MARKSCAN to create .BSR (bottle scan records) file from .MRK file, created by hitting (cntrl-f5) after a bottle is tripped.]

(1)	Convert raw frequency data to binary pressure, temperature and conductivity using SEABIRD's DATCNV program.  [.ROS file is based on either bottle flags within the data stream (normal), or on information from the .BSR file (manual procedure)]

(2)	Split the file into the up and down traces using SEABIRD's SPLIT program.

(3)	Check downcast for and mark any 'wild' data points with SEABIRD's WILDEDIT program.

(4)	Filter downcast conductivity and temperature using SEABIRD's FILTER program. This is a low pass filter and we used a time constant of 0.045 seconds for conductivity and 0.15 seconds for temperature.

(5)	Mark downcast scans where the CTD is moving less than the minimum velocity of 0.10 m/s using SEABIRD's LOOPEDIT program.

(6)	Align downcast pressure, temperature and conductivity using SEABIRD's ALIGNCTD program by advancing the conductivity signal by 0.01 sec.

(7)	Apply the thermal mass correction for the conductivity cell using SEABIRD's CELLTM program.

(8)	Compute dissolved oxygen in ml/l using SEABIRD's DERIVE program.

(9)	Create WOCE 2-dbar dataset using OSD program PRO-WOCE.

(10)	Bin average downcast data to 1.0-dbar intervals using SEABIRD's BINAVG program.

(11)	Compute downcast salinity, potential density(((), potential temperature((), and depth using SEABIRD's DERIVE program.

(12)	Convert the down cast from binary to ASCII using SEABIRD's TRANS program.

(13)	Convert downcast to ODF format using PCS program SEAODF.

(14)	Create IGOSS message using PCS program ODF_IGOS.

(15)	Prepare batch and command files to transfer the data to the VAX and create the input for SEABIRD's ROSSUM program using our customized MAKEFILE program.

(16)	Check for bottles, then use ROSSUM to create the rosette summary file.

(17)	Convert the resulting .BTL file to a format suitable for ingestion into Quattro PRO (.QAT file) using our customized QPROBTL program.

(18)	Create the calibration file of merged up- and down-cast data using OSD program CALIB.

(19)	Perform the FTP transfer of the raw binary and processed data to the VAX using OSD program CTD.XFER.

(20)	Copy Quattro, downcast, and ODF files to appropriate directories and clean up.

Plots and status info displayed by the SEASAVE program during the acquisition are discarded when the program terminates.  The post-processing plotting was not included in the batch job because SEABIRD's SEAPLOT program requires interactive operator attention.  Plots produced after each station include T, S, O2, and ((  vs. pressure and T vs. S.  Section plots were produced with Igor Yakashev’s contour package, modified to accept .ODF files.

5b.  Calibration

At the base of each CTD cast two rosette bottles were tripped, one of which carried a pair of digital thermometers (T347,T352). Salinity samples were drawn from each of the two bottles and analyzed onboard with an Guildline AutoSal salinometer.  The comparison of these standards against the SeaBird CTD (Table 2a below) shows that, after the removal of several obvious outliers, the offset in temperature is negligible, but that for salinity is significantly different from zero. Nevertheless, the standard deviations about the offsets are small and could be easily be explained by the differences in the “replicate” standards (the two salinity standards are not true replicates since they come from different bottles, tripped sequentially), so the calibrations for both T and S are considered generally acceptable.

The performance of the YSI O2 sensor was similar to that on previous cruises.  The surface values on the downtrace appeared to be fully equilibrated, thanks to a 3 min. waiting period (as suggested by the manufacturer), but there was usually a large hysteresis between the down- and uptraces in the vicinity of the pycnocline, and there were occasional spikes from the electronics.  The hysteresis probably results from a mismatch of the temperature and O2 sensors in the probe and might be improved by applying filters with appropriate phase lags. The dissolved oxygen samples collected from calibration bottles were analyzed on board with the automated titration unit borrowed from Marine Chemistry. These “replicates” agreed to within a standard deviation of 0.07 ml/l (Table 2a).  Comparisons between the YSI measurements and bottle samples revealed a small offset between the sensor and titrated values (Table 2a). After removal of significant outliers (based on replicate statistics), a linear regression analysis of titrated on sensor values at the bottom provides an effective calibration (Table 2b; Fig.2) with high correlation and low standard error ((0.07 ml/l).

Problems/Recommendations:

(1)	The aging General Oceanics rosettes should be replaced with SEABIRD systems as soon as possible to improve reliability of bottle tripping and data capture.

(2)	True replicate salinity and O2 samples should be drawn in future to remove the ambiguity involved in assessing the calibration standards.

(3)	Efforts should be made to remove the hysteresis between the up and down traces from the YSI sensor by application of filters with various lags.

5c.  Sections

CTD sections Ia,b, II, III, V, VI, and the Halifax Section (Figs. 3-9) depict hydrographic conditions, 1) along the eastern boundary of the Gulf of Maine, 2) across the sill in Northeast Channel, 3) down the western flank of Browns Bank, 4) along Truxton Swell separating Georges and Jordan Basins, 5) along the 200 m isobath on the eastern side of the Channel, 6) across the outer Scotian Shelf off Shelburne, and 7) across the entire Scotian Shelf off Halifax, respectively.  Section Ia (Fig.3) shows a surface layer of fresh water extending out from Cape Sable over the shelf, with pockets of S<31.5 near the coast and inshore edge of Browns Bank.  This contrasts with previous June sections (94018, 95010) when the freshest water (S<31.5) was found over the outer edge of Browns, with slightly higher salinities inshore.  The lowest temperatures are also found in the intermediate layer along the inshore edge of Browns.  The outer edge of Browns is stratified mainly by salinity and shows some evidence of mixing with slope waters (CTD13; Fig.3e).  Minimum oxygen values are also found near the bottom on the outer edge of the shelf.  The cold intermediate water (<5oC)  also disappears over the outer shelf.

The distribution of deep water properties on Section Ib (Fig.4) shows slope water characteristics (T>10oC, S>35, O2<4 ml/l) in the center of the Channel (CTD6) at depths of 100-200m.  The density section shows isopycnals sloping upward to the west, suggesting (geostrophically) a maximum inflow current near 100m at CTD6. Similarly, the flow between CTD4-5 would appear to be outward with a maximum somewhat higher in the water column, based on geostrophy and weak near-bottom flow. The T-S diagram (Fig.4e) gives clear evidence for interleaving between coastal and offshore water masses in the Channel.  Surface waters on Georges Bank appear to be somewhat more saline than on Browns or in the Channel by roughly 0.4.

Section II (Fig.5) shows the presence of slope water on the western flank of Browns Bank, with T>10oC and S>35 at CTD31-33.  CTD33 also shows a well-developed cold intermediate layer above the slope water, but the deeper stations some mixing with other water masses at intermediate depths.  The surface waters are freshest on the eastern side of the section, and CTD 34 appears to represent a vertically-mixed version of the top 100m of water at CTD33. The sloping isopycnals suggest inflow maxima at 50-100m at CTD32-33.  A large volume of low oxygen water (O2<4 ml/l) lies in the deeper regions of Georges Basin.

The properties along Truxton Swell (Fig.6) show no evidence for slope water intrusion, with just a hint of higher salinity and temperature water passing over the sill at CTD25.  Conditions east of that point are generally well-mixed, relative to those in the central Gulf.  The freshest surface water lies over the eastern half of the section and the T-S diagram (Fig.6e) shows some variability of intermediate layer properties at CTD28-29.

Conditions on Section V (Fig.7), from Truxton Swell to the mouth of Northeast Channel along the eastern 200m isobath, are quite variable, showing pockets of slope and cold intermediate waters at various locations and depths.  This is undoubtedly due, in part, to aliasing by the temporal variability in the Channel.  CTD 39, on the 600 m isobath off the mouth of the Channel, features warm slope water at depths of 50-150 m and warm mixtures of coastal and slope water near the surface.  Strong interleaving of these with coastal water masses occurs at CTD35-38, whereas conditions are more uniform in the vertical at the interior stations, CTD32,26 (Fig.7e).  The freshest surface water, S<31, is found near the mooring line at CTD36,37.

Section VI (Fig.8) reveals a stark contrast between classic Scotian Shelf and slope water structures.  CTD41-42 feature a warm, fresh layer overlying a cold (<2oC) intermediate layer with warmer, saltier water near the bottom.  Between CTD42 and 43 there is a transition of the intermediate and deep layers to slope water, while the surface layer remains relatively fresh and warm.  The isopycnal slopes suggest slight intensification of the presumed westward flow from the bottom up to roughly the 50m level over the shelf break.  Note also that the minimum surface salinities are found at the shelf break (CTD42-43; Fig.8e).  The cold intermediate layer is associated with very high dissolved oxygen, whereas an O2 minimum is found at depths of 150-250m in the slope water.

The Halifax Section data (Fig.9) reveal three separate surface water masses across the shelf.  Inshore (CTD50-51) the surface salinity is near 30 and the cold intermediate minimum is near 31.5; at midshelf the surface is near 30.9 and the minimum near 32.2; and finally at the shelf break, the surface is near 32 and the minimum near 33.  The intermediate temperature minimum generally increases offshore, except for an anomalous cold patch at the outer edge of the section (CTD45).  The T-S plot (Fig.9e) indicates a high degree of interleaving between shelf and slope water masses at the offshore end of the section as well.  The isopycnal slopes (Fig.9c) indicate westward flow near the coast and at the shelf break would be surface intensified, and the oxygen section (Fig.9d) shows similar values in the bottom of Bedford Basin and offshore at depths of 250-350m.

6. ADCP TRANSECTS

The RDI ADCP was run continuously over the cruise in the bottom track mode.  The velocity measurements were made in 100 4-m bins below the transducer depth (4.9 m).  In the standard acquisition mode, 10-ping ensembles were averaged over 5 minutes to create processed profiles of velocity, beam intensity, etc.  The RDI system appeared to work well over the cruise.

Ten primary transects (6 full, 4 partial; Table 3) formed the repeated ADCP section across the Channel, including CTD Sections Ib and the transits during mooring operations.  On these transects, only the averaged processed data were collected.  A total of 16 hrs was devoted to straight-run transects, with an additional 20 hrs spent on the CTD and mooring lines (transects 1,2,4).  Some of the transects (2,3,5,10) were incomplete due to operational constraints.

A calibration of the transducer alignment and amplification factor was conducted shortly after leaving BIO, on the straight run down to SW Nova Scotia.  The results (Table 3a) show that both these quantities are negligibly different from their design values of 0 deg. and 1.00, respectively.

Acknowledgements:

We are greatly indebted to the officers and crew of the C.S.S. Parizeau for their skilled assistance and friendly cooperation, which was vital to the success of this mission.

TABLE 1.  Moorings Recovered During Parizeau Cruise 97025, 27 June-4 July, 1997

Mooring	Site	N. Lat.	Recovery	Instrument 	Comments

No. 	(Depth,m)	W. Long.	Time(Z),Date	(Depth,m)

1238	SEFA	41o19.36’	1419,Jun.29	SCAT1238(24)	hairy growth, cell clear

(94)	66o28.33’		RCM4600(25)	  “  “  , rotor free,  “  “

1239	SEF	41o19.37’	1357,Jun.29	RCM7592(51)	  “  “  ,  “  “  ,  “  “

(96)	66o28.49’		RCM2664(86)	  “  “ , rotor impeded by

growth, cell clear

TG343(96)	hairy growth

1240	NECWA	42o07.78’	1948,Jun.28	SCAT1019(25)	heavy growth, cell clear

(215)	66o00.91’		RCM7122(26)	  “  “  , rotor free,  “  “

1241	NECW	42o07.64’	2250,Jun.28	RCM7525(54)	drag mooring, rotor free

(214)	66o00.75’		RCM6400(104)	  “  “  ,  “  “

RCM6411(154)	  “  “  ,  “  “

RCM6412(194)	line parted, instr. lost

TG109(214)	  “  “  ,  “  “

1242	NECEA	42o17.72’	1533,Jun.28	SCAT1237(23)	no floats, on bottom

(213)	65o50.43’		RCM9355(24)	 “  “ , “  “ , rotor free

1243	NECE	42o17.87’	1615,Jun.28	RCM7131(54)	light growth, rotor free

(214)	65o50.79’		RCM4195(104)	  “  “  ,  “  “

RCM4355(154)	clean, rotor free

RCM5577(194)	  “  ,  “  “

TG336(214)	clean

TABLE 2.  CTD Stations During Parizeau 97025, 27 June-4 July, 1997

Stn.	N.LAT.	W.LONG.	 Sound.	Date	Year	Time

No. 	(m)	Day	[UTC]

0	44.683	63.647	62	Jun 27 1997	178	15:28:00

1	42.297	65.848	215	Jun 28 1997	179	17:42:00

2	42.132	66.010	222			19:20:00

3	41.998	66.136	84	Jun 29 1997	180	02:03:02

4	42.063	66.078	89			02:54:13

5	42.132	65.992	213			04:02:32

6	42.198	65.931	221			04:57:46

7	41.733	66.533	74			10:54:00

8	41.322	66.483	94			13:35:00

9	41.778	66.344	75			17:51:13

10	42.268	65.868	223			21:36:54

11	42.336	65.797	190			22:36:17

12	42.425	65.747	96			23:33:46

13	42.500	65.740	84	Jun 30 1997	181	00:29:11

14	42.583	65.743	88			01:37:57

15	42.672	65.746	86			02:44:06

16	42.752	65.758	99			04:39:38

17	42.835	65.756	98			05:40:31

18	42.920	65.754	145			06:32:30

19	43.000	65.750	128			07:29:47

20	43.086	65.745	91			08:26:18

21	43.166	65.745	52			10:28:54

22	43.247	65.745	41			11:24:29

23	43.278	66.437	63			15:52:12

24	43.215	66.647	108			17:08:15

25	43.171	66.865	160			18:35:14

26	43.136	67.102	178			20:06:17

27	43.169	67.318	191			21:33:00

28	43.121	67.556	178			23:06:01

29	43.001	67.739	167	Jul 01 1997	182	00:36:10

30	42.925	67.996	168			03:16:00

31	42.507	66.960	324			09:24:00

32	42.591	66.779	222			10:58:00

33	42.707	66.612	166			12:33:00

34	42.801	66.434	100			13:49:00

35	42.509	66.179	217			16:20:54

36	42.426	65.980	217			17:41:41

37	42.299	65.846	212			19:01:47

38	42.192	65.702	214	Jul 02 1997	183	11:30:27

39	42.092	65.511	617			13:17:41

40	42.177	65.499	114			14:23:56

41	42.894	64.501	100			21:14:29

42	42.751	64.362	113			22:45:53

43	42.678	64.294	232 			23:45:56

44	42.609	64.226	934	Jul 03 1997	184	00:58:34

45	42.850	61.732	506			12:45:25

46	43.000	61.895	149			14:15:36

47	43.183	62.100	97			15:57:03

48	43.484	62.451	80			18:26:39

49	43.884	62.884	259			22:19:21

50	44.267	63.317	150	Jul 04 1997	185	01:38:26

51	44.401	63.450	80			02:59:58

______________________________________________________________________________

TABLE 2a. Temperature and Salinity Calibration Results for Parizeau 97025

QUANTITY	  NO. SAMPLES	MEAN DIFF.	STD. DEV.

CTD vs. Standard

Salinity:

CTD-AutoSal.	73	-0.024	0.011

Temperature:

CTD-Thermometers	77	-0.002	0.020

Dissolved Oxygen:

YSI-Titration(1-41)	91	 -0.22	0.08

Standard vs. Standard

Salinity:

Btl.1-Btl.2.	39	-0.003	0.025

Temperature:

T878-T881	38	 0.001	0.004

Dissolved Oxygen:

Btl.1-Btl.2.(1-41)	45	  -0.003	0.071

______________________________________________________________________________

TABLE 2b. Dissolved Oxygen Regression Results for Parizeau 97025

Y = aX+b  (Y=titration, X=sensor)

SENSOR(CTD)	NO. SAMPLES	a((a	b((b(ml/l)	   ((Y(ml/l)	r2

YSI(1-41)	91	1.0404(0.0083	0.023(0.023   (0.070	.994	0.98

______________________________________________________________________________

______________________________________________________________________________

TABLE 3  Primary ADCP Transects During Parizeau 97-025

NO.	DATE	STRT	END	FROM	TO	COMMENTS

(m-d)	(UTC)	(UTC)	(Lat./Long.)	(Lat./Long.)

1	06-28	14:45	01:50	42°25'/65°45'	42°00'/66°08'	moorings

2	06-29	02:00	05:00	42°00'/66°08'	42°12'/65°56'	CTD3-6

3	06-	05:00	06:30	42°12'/65°56'	42°00'/66°08'	CTD6-NEP

4	06-	18:30	23:50	42°00'/66°08'	42°26'/65°44'	CTD9-12

5	07-01	18:50	20:00	42°18'/65°51'	42°26'/65°45'	CTD37,partial

6	07-	20:14	23:19	42°26'/65°45'	42°00'/66°09'

7	07-	23:19	02:20	42°00'/66°09'	42°26'/65°45'

8	07-02	02:28	05:40	42°26'/65°45'	42°00'/66°09'

9		07-	05:50	09:09	42°00'/66°09'	42°26'/65°45'

10	07-	09:09	10:10	42°26'/65°45'	42°18'/65°51'	 partial

______________________________________________________________________________

TABLE 3a.  Straight Run RDI Calibrations for Parizeau 97-025

DATE:		27 June, 1997

TIME		MISALIGNMENT ANGLE              AMPLIFICATION FACTOR

(deg.)		(-)

22:27:41	-2.237	1.032

22:32:45	 0.300	1.039

22:37:49	-0.140	0.975

22:42:44	-1.207	1.019

22:47:49	-1.102	0.997

22:52:44	-0.369	1.012

22:57:49	-1.100	1.003

AVERAGE	-0.737	1.008

______________________________________________________________________________

FIGURE CAPTIONS:

Figure 1	a) Mooring sites, and b) CTD positions and ADCP transects for C.S.S. Parizeau

Cruise 97-025, 27 June-4 July 1997

Figure 2	Calibration data for the YSI dissolved oxygen sensor. Titrated values from rosette bottle samples are plotted against uptrace values from the sensor at the same depth.  Bold line through the points is a linear regression of titrated on sensor values (Table 2b).  Dashed and dotted lines represent calibrations from data other than those plotted.

Figure 3	Hydrographic section Ia (CTD22-12) from Cape Sable to the offshore edge of

Browns Bank.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 4	Hydrographic section Ib (CTD3-6,10-12) across Northeast Channel at the mooring line.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 5	Hydrographic section II (CTD34-31) on the western flank of Browns Bank.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 6	Hydrographic section III (CTD23-30) aolng Truxton Swell.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 7	Hydrographic section V (CTD26,32,35-39) along the slope water inflow axis ((200m isobath) from Georges Basin to the mouth of Northeast Channel.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 8	Hydrographic section VI (CTD41-44) across the Scotian Shelf break off Shelburne.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map

Figure 9	Halifax hydrographic section  (CTD45-50) from the Scotian Shelf break to Halifax.

(a) temperature,

(b) salinity,

(c) sigma-(,

(d) dissolved oxygen,

(e) temperature vs. salinity, and

(f) station map